## Slide 1: Class 07: Outline
Hour 1:
Conductors & Insulators
Expt. 2: Electrostatic Force
Hour 2:
Capacitors

## Slide 2: Last Time: Gauss’s Law

## Slide 3: Gauss’s Law
In practice, use symmetry:
Spherical (r)
Cylindrical (r, )
Planar (Pillbox, A)

## Slide 4: Conductors

## Slide 5: Conductors and Insulators
A conductor contains charges that are free to move (electrons are weakly bound to atoms)
Example: metals
An insulator contains charges that are NOT free to move (electrons are strongly bound to atoms)
Examples: plastic, paper, wood

## Slide 6: Conductors
Conductors have free charges
 E must be zero inside the conductor
 Conductors are equipotential objects
Neutral Conductor
-
-
-
-
+
+
+
+
E

## Slide 7: Equipotentials

## Slide 8: Topographic Maps

## Slide 9: Equipotential Curves
All points on equipotential curve are at same potential.
Each curve represented by V(x,y) = constant

## Slide 10: PRS Question: Walking down a mountain

## Slide 11: Direction of Electric Field E
E is perpendicular to all equipotentials
Constant E field
Point Charge
Electric dipole

## Slide 12: Properties of Equipotentials
E field lines point from high to low potential
E field lines perpendicular to equipotentials
  Have no component along equipotential
  No work to move along equipotential

## Slide 13: Conductors in Equilibrium
Conductors are equipotential objects:
1) E = 0 inside
2) Net charge inside is 0
3) E perpendicular to surface
4) Excess charge on surface

## Slide 14: Conductors in Equilibrium
Put a net positive charge anywhere inside a conductor, and it will move to the surface to get as far away as possible from the other charges of like sign.
Java applet link

## Slide 15: Expt. 2: Electrostatic Force
Link to Movie of Experiment

## Slide 16: Expt. 2: Electrostatic Force
Java Applet for Force Experiment

## Slide 17: Experiment 2: Electrostatic Force

## Slide 18: Capacitors and Capacitance

## Slide 19: Capacitors: Store Electric Energy
Capacitor: two isolated conductors with equal and opposite charges Q and potential difference V between them.
Units: Coulombs/Volt or Farads

## Slide 20: Parallel Plate Capacitor

## Slide 21: Parallel Plate Capacitor
When you put opposite charges on plates, charges move to the inner surfaces of the plates to get as close as possible to charges of the opposite sign
Link to capacitor applet

## Slide 22: Calculating E (Gauss’s Law)
Note: We only “consider” a single sheet! Doesn’t
the other sheet matter?

## Slide 23: Alternate Calculation Method
+ + + + + + + + + + + + + +
Top Sheet:
- - - - - - - - - - - - - -
Bottom Sheet:

## Slide 24: Parallel Plate Capacitor
C depends only on geometric factors A and d

## Slide 25: Demonstration: Big Capacitor

## Slide 26: Spherical Capacitor
Two concentric spherical shells of radii a and b
Gauss’s Law  E ≠ 0 only for a < r < b, where it looks like a point charge:
What is E?

## Slide 27: Spherical Capacitor
For an isolated spherical conductor of radius a:
Is this positive or negative? Why?

## Slide 28: Capacitance of Earth
For an isolated spherical conductor of radius a:
A Farad is REALLY BIG! We usually use pF (10-12) or nF (10-9)

## Slide 29: 1 Farad Capacitor
How much charge?

## Slide 30: PRS Question: Changing C Dimensions

## Slide 31: Demonstration: Changing C Dimensions

## Slide 32: Energy Stored in Capacitor

## Slide 33: Energy To Charge Capacitor
1. Capacitor starts uncharged.
2. Carry +dq from bottom to top.
Now top has charge q = +dq, bottom -dq
3. Repeat
4. Finish when top has charge q = +Q, bottom -Q
+q
-q

## Slide 34: Work Done Charging Capacitor
At some point top plate has +q, bottom has –q
Potential difference is V = q / C
Work done lifting another dq is dW = dq V
+q
-q

## Slide 35: Work Done Charging Capacitor
So work done to move dq is:
Total energy to charge to q = Q:
+q
-q

## Slide 36: Energy Stored in Capacitor
Since
Where is the energy stored???

## Slide 37: Energy Stored in Capacitor
Parallel-plate capacitor:
Energy stored in the E field!

## Slide 38: 1 Farad Capacitor - Energy
How much energy?
Compare to capacitor charged to 3kV:

## Slide 39: PRS Question: Changing C Dimensions Energy Stored

## Slide 40: Demonstration: Dissectible Capacitor