## Slide 1: Class 21: Outline
Hour 1:
Expt. 9: Faraday’s Law
Hour 2:
Faraday’s Law
Transformers
Magnetic Materials

## Slide 2: Last Time: Faraday’s Law

## Slide 3: Faraday’s Law of Induction
Changing magnetic flux induces an EMF
Lenz: Induction opposes change

## Slide 4: What can change?
Quantities which can vary with time:
Magnitude of B
Area A enclosed by the loop
Angle  between B and loop normal

## Slide 5: Magnet Falling Through a Ring
Falling magnet slows as it approaches a copper ring which has been immersed in liquid nitrogen.
Link

## Slide 6: Example: Magnitude of B Magnet Falling Through a Ring
Falling magnet approaches a copper ring
or Copper Ring approaches Magnet

## Slide 7: Moving Towards Dipole
As ring approaches, what happens to flux?
It increases
Move ring down

## Slide 8: Moving Over Dipole
Flux increases then decreases
Note we have arbitrarily assigned dA up
Flux
Move down

## Slide 9: Moving Over Dipole
Current first goes in one direction, then other
It ALWAYS opposes the changing flux
Move down
Current
CW
CCW

## Slide 10: Five PRS Questions: Predictions for Experiment 9 Faraday’s Law

## Slide 11: Experiment 9: Faraday’s Law of Induction

## Slide 12
CURRENT
FLUX
Imperfect
current 0

## Slide 13: Four PRS Questions: Force on A Loop Below Magnet Moving Upward; Moving Rail; Moving Rectangle near Wire; Generator.

## Slide 14: Brakes

## Slide 15: Magnet Falling Through a Ring
What happened to kinetic energy of magnet?

## Slide 16: Eddy Current Braking
What happened to kinetic energy of pendulum?
http://demoroom.physics.ncsu.edu/html/demos/163.html

## Slide 17: Eddy Current Braking
What happened to kinetic energy of disk?
http://demoroom.physics.ncsu.edu/multimedia/video/5K20.22.1.MOV

## Slide 18: Demonstration: Eddy Current Braking

## Slide 19: Eddy Current Braking

The magnet induces currents in the metal that dissipate the energy through Joule heating:
XX
XX
Current is induced counter-clockwise (out from center)
Force is opposing motion (creates slowing torque)

## Slide 20: Eddy Current Braking

The magnet induces currents in the metal that dissipate the energy through Joule heating:
XX
XX
Current is induced clockwise (out from center)
Force is opposing motion (creates slowing torque)
EMF proportional to 


## Slide 21: Demonstration: Levitating Magnet Superconductor & Magnet
Link

## Slide 22: PRS Questions: Loop in Uniform Field

## Slide 23: Mutual Inductance

## Slide 24: Mutual Inductance
A current I2 in coil 2, induces some magnetic flux 12 in coil 1. We define the flux in terms of a “mutual inductance” M12:

## Slide 25: Demonstration: Remote Speaker

## Slide 26: Transformer
Step-up transformer
Ns > Np: step-up transformer
Ns < Np: step-down transformer

## Slide 27: Demonstrations: One Turn Secondary: Nail Many Turn Secondary: Jacob’s Ladder

## Slide 28: Transmission of Electric Power
Power loss can be greatly reduced if transmitted at high voltage

## Slide 29: Example: Transmission lines
An average of 120 kW of electric power is sent from a power plant. The transmission lines have a total resistance of 0.40 . Calculate the power loss if the power is sent at (a) 240 V, and (b) 24,000 V.
(a)
(b)
83% loss!!
0.0083% loss

## Slide 30: Magnetic Materials

## Slide 31: Recall Polar Dielectrics
Dielectric polarization decreases Electric Field!

## Slide 32: Para/Ferromagnetism
Applied external field B0 tends to align the atomic magnetic moments

## Slide 33: Para/Ferromagnetism
The aligned moments tend to increase the B field
Compare to:

## Slide 34: Para/Ferromagnetism
Paramagnet: Turn off B0, everything disorders
Ferromagnet: Turn off B0, remains (partially) ordered
This is why some items you can pick up with a magnet even though they don’t pick up other items

## Slide 35: Magnetization Vector
Useful to define “Magnetization” of material:
M=0
M>0

## Slide 36: Hysteresis in Ferromagnets
The magnetization M of a ferromagnetic material depends on the history of the substance
Magnetization remains even with B0 off !!!