## Slide 1: Class 18: Outline
Hour 1:
Levitation
Experiment 8: Magnetic Forces
Hour 2:
Ampere’s Law

## Slide 2: Review: Right Hand Rules
Torque: Thumb = torque, fingers show rotation
Feel: Thumb = I, Fingers = B, Palm = F
Create: Thumb = I, Fingers (curl) = B
Moment: Fingers (curl) = I, Thumb = Moment

## Slide 3: Last Time: Dipoles

## Slide 4: Magnetic Dipole Moments
Generate:
Feel:
1) Torque to align with external field
2) Forces as for bar magnets (seek field)

## Slide 5: Some Fun: Magnetic Levitation

## Slide 6: Put a Frog in a 16 T Magnet…
For details: http://www.hfml.sci.kun.nl/levitate.html

## Slide 7: How does that work? First a BRIEF intro to magnetic materials

## Slide 8: Para/Ferromagnetism
Applied external field B0 tends to align the atomic magnetic moments (unpaired electrons)

## Slide 9: Diamagnetism
Everything is slightly diamagnetic. Why? More later.
If no magnetic moments (unpaired electrons) then this effect dominates.

## Slide 10: Back to Levitation

## Slide 11: Levitating a Diamagnet
Create a strong field (with a field gradient!)
Looks like a dipole field
Toss in a frog (diamagnet)
Looks like a bar magnet pointing opposite the field
Seeks lower field (force up) which balances gravity
S
N
N
S
Most importantly, its stable:
Restoring force always towards the center
S
N

## Slide 12: Using B to Levitate
For details: http://www.hfml.ru.nl/levitation-movies.html
Frog
Strawberry
Water Droplets
Tomatoes
Crickets

## Slide 13: Demonstrating: Levitating Magnet over Superconductor

## Slide 14: Perfect Diamagnetism: “Magnetic Mirrors”
N
S
N
S

## Slide 15: Perfect Diamagnetism: “Magnetic Mirrors”
N
S
N
S
No matter what the angle, it floats -- STABILITY

## Slide 16: Using B to Levitate
For details: http://www.hfml.sci.kun.nl/levitate.html
A Sumo Wrestler

## Slide 17: Two PRS Questions Related to Experiment 8: Magnetic Forces

## Slide 18: Experiment 8: Magnetic Forces (Calculating 0)
Animation

## Slide 19: Experiment Summary: Currents feel fields Currents also create fields Recall… Biot-Savart

## Slide 20: The Biot-Savart Law
Current element of length ds carrying current I produces a magnetic field:

## Slide 21: Today: 3rd Maxwell Equation: Ampere’s Law
Analogous (in use) to Gauss’s Law

## Slide 22: Gauss’s Law – The Idea
The total “flux” of field lines penetrating any of these surfaces is the same and depends only on the amount of charge inside

## Slide 23: Ampere’s Law: The Idea
In order to have a B field around a loop, there must be current punching through the loop

## Slide 24: Ampere’s Law: The Equation
The line integral is around any closed contour bounding an open surface S.
Ienc is current through S:

## Slide 25: PRS Question: Ampere’s Law

## Slide 26: Biot-Savart vs. Ampere
Biot-Savart Law
general
current source
ex: finite wire
wire loop
Ampere’s law
symmetric
current source
ex: infinite wire
infinite current sheet

## Slide 27: Applying Ampere’s Law
Identify regions in which to calculate B field Get B direction by right hand rule
Choose Amperian Loops S: Symmetry B is 0 or constant on the loop!
Calculate
Calculate current enclosed by loop S
Apply Ampere’s Law to solve for B

## Slide 28: Always True, Occasionally Useful
Like Gauss’s Law,
Ampere’s Law is always true
However, it is only useful for calculation in certain specific situations, involving highly symmetric currents.
Here are examples…

## Slide 29: Example: Infinite Wire
I
A cylindrical conductor has radius R and a uniform current density with total current I
Find B everywhere
Two regions:
(1) outside wire (r ≥ R)
(2) inside wire (r < R)

## Slide 30: Ampere’s Law Example: Infinite Wire
I
I
B
Amperian Loop:
B is Constant & Parallel
I Penetrates

## Slide 31: Example: Wire of Radius R
Region 1: Outside wire (r ≥ R)
Cylindrical symmetry 
Amperian Circle
B-field counterclockwise

## Slide 32: Example: Wire of Radius R
Region 2: Inside wire (r < R)
Could also say:

## Slide 33: Example: Wire of Radius R

## Slide 34: Group Problem: Non-Uniform Cylindrical Wire
I
A cylindrical conductor has radius R and a non-uniform current density with total current:
Find B everywhere

## Slide 35: Applying Ampere’s Law
In Choosing Amperian Loop:
Study & Follow Symmetry
Determine Field Directions First
Think About Where Field is Zero
Loop Must
  Be Parallel to (Constant) Desired Field
  Be Perpendicular to Unknown Fields
  Or Be Located in Zero Field

## Slide 36: Other Geometries

## Slide 37: Helmholtz Coil

## Slide 38: Closer than Helmholtz Coil

## Slide 39: Multiple Wire Loops

## Slide 40: Multiple Wire Loops – Solenoid

## Slide 41: Magnetic Field of Solenoid
loosely wound
tightly wound
For ideal solenoid, B is uniform inside & zero outside

## Slide 42: Magnetic Field of Ideal Solenoid
Using Ampere’s law: Think!

## Slide 43: Demonstration: Long Solenoid

## Slide 44: Group Problem: Current Sheet
A sheet of current (infinite in the y & z directions, of thickness 2d in the x direction) carries a uniform current density:
Find B everywhere
y

## Slide 45: Ampere’s Law: Infinite Current Sheet
I
Amperian Loops:
B is Constant & Parallel OR Perpendicular OR Zero
I Penetrates
B
B

## Slide 46: Solenoid is Two Current Sheets
Field outside current sheet should be half of solenoid, with the substitution:
This is current per unit length (equivalent of , but we don’t have a symbol for it)

## Slide 47: Ampere’s Law: .
=
2 Current Sheets
I
B
B
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
B
Long
Circular
Symmetry
(Infinite) Current Sheet
Solenoid
Torus

## Slide 48: Brief Review Thus Far…

## Slide 49: Maxwell’s Equations (So Far)